## Slide 1: Combinational Logic Continued; Memory and Sequential Circuits Part 1: Boolean Functions
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 2: Road Map
Central processing unit (CPU)
(microprocessors)
Memory
Sequential circuits
electricity
combinational logic
logic gates
circuits
transistors
materials
✔
✔
✔
✔
✔

## Slide 3: Boolean Functions
Goal: Design a circuit to implement an arbitrary Boolean function on n binary inputs:
y = f (x1, x2, … xn)
f()
x1
x2
x3
xn
y
…

## Slide 4: Example: Adder Circuit
Binary addition: Add two n-bit numbers
An-1 … A1A0 + Bn-1 … B1B0 -> Sn-1 … S1S0
0 0 1 1 0 1
0 0 1 1 0 0
0 1 1 0 0 1
+
carry
FA
FA
FA
B0
A0
B1
A1
Bn-1
An-1
S0
S1
Sn-1
C0
C1
C2
Cn-1
Cn
…
Ripple Carry Adder
Assuming 2’s complement:
What is C0?
What do we do with Cn?
1 bit adder: full adder (FA)
Inputs: Ai, Bi, Ci
Outputs: Si, Ci+1
FA
Bi
Ai
Si
Ci
Ci+1
Ci
Ci+1
Ai
Bi
Si
Our strategy for addition is to develop a Boolean function (and then a circuit) whose output is equivalent to addition
Notes: Related: How do we detect overflow?

## Slide 5: Example: Sum Output
Ai Bi Ci
Si
Consider addition with inputs Ai and Bi along with a carry bit Ci. Determine the corresponding sum bit Si and the next carry bit Ci+1.
Ci+1

## Slide 6: Example: Sum Output
Ai Bi Ci
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Si
0
1
1
0
1
0
0
1
Ci+1
0
0
0
1
0
1
1
1

## Slide 7: Full Adder: Sum Output
Ai Bi Ci
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Si
0
1
1
0
1
0
0
1
A
B
C
A
B
C
A
B
C
A
B
C
Output
Any truth table can be converted to a Boolean equation
Any Boolean equation can be implemented by a circuit
Therefore, any logic function can be realized with a circuit
Caveats: (1) In practice, number of inputs (fanin), outputs (fanout) for a gate limited, but there are ways around this; (2) above approach may not yield optimal circuits in terms of number of gates or delay
Any logic function can be completely specified by a truth table
Si = AiBiCi
+ AiBiCi + AiBiCi + AiBiCi

## Slide 8: Canonical Sum of Products Form
Si = AiBiCi
+ AiBiCi + AiBiCi + AiBiCi
Ai Bi Ci
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Si
0
1
1
0
1
0
0
1
Canonical sum of products representation
  Boolean equation is a sum (i.e., or) of product terms (i.e., and)
  Each product term includes all input variables, either complemented or not complemented (aka minterm)
One can often derive simpler Boolean equations which typically leads to fewer gates (not discussed here)
  Methods exist to minimize the number of gates
minterm
Every row whose output is one gets a term; these terms are added (OR’d)
Each term is the product (AND) of each input or its complement (whichever is 1) with the other inputs (or their complements)

## Slide 9: Full Adder Circuit
Ai Bi Ci
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Si
0
1
1
0
1
0
0
1
Ci+1
0
0
0
1
0
1
1
1
A
B
C
A
B
C
A
B
C
A
B
C
Si
A
B
C
A
B
C
A
B
C
A
B
C
Ci+1
23=8 different input combinations
4 lead to Si=1
4 lead to Ci+1=1
1 overlaps; 1 results in Si=Ci+1=0

## Slide 10: Examples: Circuits  Truth Tables
Ai Bi
0 0
0 1
1 0
1 1
Z
1
1
0
0
A
B
A
B
A
B
Z
Write the truth table that corresponds to the circuit.
Draw the circuit that corresponds to the truth table.

## Slide 11: Examples: Circuits  Truth Tables
Ai Bi
0 0
0 1
1 0
1 1
Z
1
1
0
1
A
B
A
B
Z
Ai Bi
0 0
0 1
1 0
1 1
Z
1
1
0
0
A
B
A
B
A
B
Z

## Slide 13: Combinational Logic Continued; Memory and Sequential Circuits Part 2: Combinational Logic Ciruits
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 14: DeMorgan’s Law
A B A+B
0 0 0
0 1 1
1 0 1
1 1 1
Start with OR function:
Complement inputs
Perform an AND
Complement output
A
1
1
0
0
B
1
0
1
0
AB
1
0
0
0
AB
0
1
1
1
A+B = AB
This:
is equivalent to
One can create an equivalent circuit by (1) converting an OR gate into an AND gate and (2) complement the gate’s inputs and outputs
It can be shown: one can also create an equivalent circuit by (1) converting an AND gate to an OR gate and (2) complementing the gate’s inputs and outputs
A or B is equivalent to not (not A and not B)
E.g.: “The pen is red or blue” is equivalent to “it is not the case that the pen is both not red and not blue”

## Slide 15: Applying DeMorgan’s Law
We can implement any logic circuit using only NAND gates
  Inverter is a NAND gate with a single input (equivalent to X nand X)
  Recall our CMOS circuits readily implemented NAND (and NOR), but AND (and OR) required an extra inverter
  NAND implementation faster, requires less silicon area than AND/OR
A
B
C
A
B
C
A
B
C
A
B
C
Output
Output = ABC + ABC + ABC + ABC
A
B
C
A
B
C
A
B
C
A
B
C
Output
Replace OR gate with a NAND gate with complemented inputs

## Slide 16: NAND-Only Full Adder Circuit
Ai Bi Ci
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Si
0
1
1
0
1
0
0
1
Ci+1
0
0
0
1
0
1
1
1
A
B
C
A
B
C
A
B
C
A
B
C
Si
A
B
C
A
B
C
A
B
C
A
B
C
Ci+1
A
B
C
A
B
C
A
B
C
A
B
C
Si
A
B
C
A
B
C
A
B
C
A
B
C
Ci+1
Original
NAND-only

## Slide 17: Fast Addition
Assume delay of 𝝉 for a signal to travel through a single gate
How many gate delays for one addition (Big-O)?
Carry Lookahead (CLA) adder
  Cluster full adders into groups (e.g., 4 full adders per group)
  CLA circuit computes carry out of a group of full adders quickly
  CLA tree can perform N-bit addition in O(log N) gate delays
FA
FA
FA
B0
A0
B1
A1
Bn-1
An-1
S0
S1
Sn-1
C0
C1
C2
Cn-1
Cn
…
Ripple
Carry
Adder
FA
FA
FA
FA
FA
FA
FA
FA
FA
FA
FA
FA
CLA
CLA

## Slide 18: Useful Boolean Algebra Laws
Law | AND | OR
Identity | A 1 = A | A + 0 = A
Null | A 0 = 0 | A + 1 = 1
Idempotent | AA = A | A + A = A
Complement | = | 
Commutative | AB = BA | A + B = B + A
Associative | (AB)C = A(BC) | (A+B)+C = A+(B+C)
De Morgan | = | =
Law | AND | OR
Identity | A 1 = A | A + 0 = A
Null | A 0 = 0 | A + 1 = 1
Idempotent | AA = A | A + A = A
Complement |  | 
Commutative | AB = BA | A + B = B + A
Associative | (AB)C = A(BC) | (A+B)+C = A+(B+C)
De Morgan |  | 
A, B, and C are Boolean variables
De Morgan’s Law: the gates within each box are equivalent
NAND
NOR

## Slide 19: Logical Completeness
For any Boolean logic function a circuit realization can be obtained using AND, OR, NOT gates
The set {AND, OR, NOT} is said to be logically complete (sufficient to implement any Boolean function)
The set {NAND} is also logically complete
NOT
AND
OR
One can show that {NOR} is logically complete
Logical completeness + memory allow one to create a machine that can compute anything that is computable (Turing machine)
Convert OR into (NOT A) NAND (NOT B)

## Slide 20: Arithmetic / Logic Unit (ALU)
Generalization of adder circuit that can perform
  Arithmetic (addition, subtraction)
  Logic operations (AND, OR, NOT)
More sophisticated ALUs can perform multiplication, division, however these operations take much longer to perform
n-bit ALU
A
(n bits)
B
(n bits)
R
(n bits)
Op
(operation)

## Slide 21: Combinational Logic Circuits
Properties
No feedback signals
Output only a function of current inputs; change the inputs and the outputs immediately (ignoring circuit delays) change
No memory; output independent of previous operations and inputs
The circuits discussed so far are called combinational logic circuits
Combinational
Logic
Inputs
x1,x2, … xr
Outputs
y1,y2, … ys
yi = fi (x1,x2, … xr)

## Slide 22: Summary
Boolean Algebra enables us to create arbitrary Boolean functions from logic gates (logical completeness)
Logic functions enable us to implement basic computational operations (e.g., arithmetic)

## Slide 24: Combinational Logic Continued; Memory and Sequential Circuits Part 3: Memory and Sequential Circuits
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 25: Road Map
central processing unit (CPU)
(microprocessors)
memory
sequential circuits
electricity
combinational logic
circuits
transistors
materials
✔
✔
✔
✔
✔
✔
logic gates

## Slide 26: Clock Signal
Clock signal used in all CPUs today
  “Advertised” clock rate indicates the frequency of this clock signal, e.g. 1.0 GHz, or 1 nanosecond (10-9 second) clock cycle time
Used in synchronous circuits (state machines)
  Asynchronous circuits do not use a clock
Clock
‘1’
‘0’
time
Clock
3𝝉
clock cycle
A
Ā
A
Ā
A=Ā ???
𝝉
𝝉 = switching time of gate
Anext=Ā
Introduce feedback

## Slide 27: Memory: D Latch (aka D Flip Flop)
Stores 1 bit of information
Inputs:
D: data input
WE: write enable
State only changes on rising edge of clock (C)
Output:
Q: data stored
D
WE
Q
C
D Latch
(flip flop)
‘1’
‘0’
time
clock
signal
C WE D Q operation
1 d d write D into flip flop storage
0 - q maintain current state (no action)
- - q maintain current state
anything
else

## Slide 28: n-Bit Register
D
WE
Q
D
WE
Q
D
WE
Q
D
WE
Q
…
WE
D0
D1
D2
Dn-1
Q0
Q1
Q2
Qn-1
A register is an array of D flip flops
WE=1: write data (D) into register (next rising edge of clock)
WE=0: register retains data last written into it
WE
D
Q
…
Clock signal not shown

## Slide 29: Random Access Memory (RAM)
Array of registers (2D array of D flip flops)
2n registers each holds a single “chunk” of data (k bits)
Can read or write a single “chunk” at a time
  Control lines: Read, Write (assert to read/write data at address A)
Address: n-bit binary number indicating which chunk (2n chunks)
k
bits
2n
registers
RAM
Write
DI (k bits)
DO (k bits)
A
(n bits)
D: data
A: address
Read
Logical view
Circuit view

## Slide 30: Binary and Unary Encoding
Given a set of N items: 0, 1, 2, … N-1
We want to select one of them
0
1
2
3
4
5
6
7
Example, N=8
Binary encoding: 011
Unary encoding:
0 0 0 1 0 0 0 0
Decoder circuit converts binary encoding to unary

## Slide 31: Decoder: Circuit to Select a Register from a Binary Number
n inputs, 2n outputs
Exactly one output is asserted (1) for any possible input (other outputs not asserted, i.e., are 0)
Used in memory components to select a memory location
1 if ABC=111, …
1 if ABC=001, 0 otherwise
A
B
C
A
B
C
A
B
C
A
B
C
1 if ABC=000, 0 otherwise
A
B
C
A
B
C
A
B
C
A
B
C
1 if ABC=010, 0 otherwise
1 if ABC=011, …
1 if ABC=100, …
1 if ABC=101, …
1 if ABC=110, …
address
select lines

## Slide 32: RAM Implementation
decoder
address
Write
D
WE
Q
D
WE
Q
D
WE
Q
D
WE
Q
DI3
DI2
DI1
DI0
…
…
…
…
Read
DO0
DO3
DO2
DO1
Switch
C = 0 open
C = 1 closed
8x4 RAM
Static RAM: implement each D flip flop with gates

## Slide 33: Dynamic RAM
Interface similar to that defined already (addr, data, rd/wr)
Capacitor has ability to store charge
  0: no charge stored on capacitor
  1: charge stored on capacitor
Reading cell discharges capacitor (if it held a charge)
Charge “leaks” from capacitor
Additional circuitry required to periodically “refresh” data (read data and immediately write it back)
Capacitor
Select Line
Data Line
DRAM Cell
DRAM circuit board

## Slide 34: SRAM vs. DRAM
Static RAM
Retains data as long as the circuit continues to receive power
Fast access time for read and write operations
Requires more Si area than DRAM
Used in processor registers, register file, fast memory (cache)
Dynamic RAM
Charge must be “refreshed” to retain data, even with continuous power
Slower access time for read and write operations
Very compact, high density (more bits/unit Si area)
Used in “main memory” for processor
Other types of memory:
ROM, PROM, Flash, disk/tape: retain data w/o power

## Slide 35: Observations
Memory implemented as NxM array of bits
  N always a power of 2 (binary address)
  M typically a power of 2 also (e.g., 32 or 64 bits) sometimes called a “word”
Computers designed to only operate on a few specific sizes of data; sizes which can be easily packed into M bit words
  8 bits (byte): character
  16 bits: short integer
  32 bits: integer, single precision floating point
  64 bits: double precision floating point

## Slide 36: Road Map
central processing unit (CPU)
(microprocessors)
memory
sequential circuits
electricity
combinational logic
circuits
transistors
materials
✔
✔
✔
✔
✔
✔
logic gates
✔

## Slide 37: Sequential vs. Combinational Circuits
Combinational Circuits
  Outputs only depend on current input
  Output same, independent of time
  Circuit has no memory (no feedback)
Sequential Circuits (aka state machines)
  Contains memory within the circuit
  Output can depend on past inputs (history)
  Mealy machine: Output depends on current state and current inputs (not used here)
  Moore machine: Output depends on current state only

## Slide 38: Combinational vs. Sequential
Two types of “combination” locks
Combinational
Success depends only on the values, not the order in which they are set.
Sequential
Success depends on the sequence of values
(e.g, R-13, L-22, R-3).
Combinational: no internal memory
Sequential requires “remembering” previous input values; the memory is internal to the lock

## Slide 39: Sequential Circuits (aka Finite State Machines [FSM])
Two key functions must be determined
Next state function: fns (current state, input)
Output function: fo (current state)
state
register
combinational logic
(next state function)
outputs
combinational logic
(output function)
fo
current
state
next
state
inputs
fns

## Slide 40: Finite State Machine Design
The behavior of combinational logic is specified by a truth table
The behavior of a finite state machine is specified by a state diagram
Finite state machine design procedure
  Develop state diagram
  Determine next state function (comb. logic)
  Determine output function (comb. logic)

## Slide 41: Example: Candy Machine
Design controller for a vending machine
Candy costs $0.15
Input signals
  N: asserted (is ‘1’) if $0.05 coin inserted
  D: asserted if $0.10 coin inserted
  At most one input asserted at a time
  N/D ignored while candy being dispensed
Output signal
  C: asserted for 1 clock cycle to dispense candy
No other coins are accepted
Machine gives no change!

## Slide 42: State Diagram
Try to put together the pieces for a state diagram for this setup.
  What are the states for the system?
  What are the transitions that can exist among the states?
Hint: aim for 4 states and 9 transitions. Note that a transition can include staying in the same state!
Design controller for a vending machine
Candy costs $0.15
Input signals
  N: asserted (is ‘1’) if $0.05 coin inserted
  D: asserted if $0.10 coin inserted
  At most one input asserted at a time
  N/D ignored while candy being dispensed
Output signal
  C: asserted for 1 clock cycle to dispense candy
No other coins are accepted
Machine gives no change!

## Slide 43: State Diagram
What are the states for the system?
  0 cents accepted
  5 cents accepted
  10 cents accepted
  >=15 cents -> triggers candy release
What are the transitions that can exist among the states?
  From 0 cents, to 5 or 10 cents.
  From 5 cents, to 10 or candy.
  From 10 cents, to candy.
  From candy, to 0 cents.
  From 0/5/10 cents, can stay put.
Design controller for a vending machine
Candy costs $0.15
Input signals
  N: asserted (is ‘1’) if $0.05 coin inserted
  D: asserted if $0.10 coin inserted
  At most one input asserted at a time
  N/D ignored while candy being dispensed
Output signal
  C: asserted for 1 clock cycle to dispense candy
No other coins are accepted
Machine gives no change!

## Slide 44: State Diagram
Circle indicates a state
  Output specified in state
Arc indicates state transition
Arc label: <input>
start
$.05
$.10
Candy
C=1
Assign each state a unique binary value (state assignment)
00
01
10
11
C=1

## Slide 45: Next State and Output Functions
Q1 Q0 D N q1 q0 C
0 0 0 0
0 0 0 1
0 0 1 0
0 1 0 0
0 1 0 1
0 1 1 0
1 0 0 0
1 0 0 1
1 0 1 0
1 1 0 0
1 1 0 1
1 1 1 0
0 0 0
0 1 0
1 0 0
0 1 0
1 0 0
1 1 0
1 0 0
1 1 0
1 1 0
0 0 1
0 0 1
0 0 1
Current State = Q1Q0
Next State = q1q0
+ +
++ +
+
+ +
00
01
10
11
C=1
One coin at a time: D and N cannot both be 1, so 12 states, not 16

## Slide 46: Candy Machine Circuit
Q1
current state
next state
Clock,WE=1
Q0
D N
q1
q0
C
+ +
++ +
+
+ +

## Slide 47: Time to Complete FSM Operations
State diagram can be used to determine time to perform operations
A state transition arc is followed each clock cycle
Example (assume 1 Hz clock)
State 00: 4 clocks waiting*, then N is asserted (5 clock cycles)
State 01: 3 clocks waiting*, then D is asserted (4 clock cycles)
State 11: 1 clock cycle
Total: 10 clock cycles or 10 seconds
00
01
10
11
C=1
* 3 and 4 are arbitrary values used for this example

## Slide 48: Summary
Memory
  Organized as a 2D array of 1-bit cells
  Well suited for fixed-sized data (e.g., 32 bits)
Sequential circuits needed whenever output depends on prior inputs (memory)
Sequential circuit design
  Construct state diagram
  Design next state function (combinational logic)
  Design output function (combinational logic)
  Put it all together (state register, next state function, output function)