## Slide 1: Instruction Set Architecture (Machine Language) Part 1: Von Neumann Machine Model
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 2: Levels of Abstraction in Computers
Application
(word processor, simulator, web browser, …)
Algorithms
(sorting, optimization, equation solver, …)
Programming Language
(C, FORTRAN, Matlab, Java, …)
Machine Instruction Set Architecture
(Intel i86, ARM, …)
Machine Organization
(Main memory, registers, adders, …)
Logic Gates
(NAND, NOR, inverter, …)
Transistors
(CMOS, NMOS, …)
Physics (Semiconductors)
(electrons, holes, …)
Operating System
(UNIX, Windows, iOS, …)
Defines interface between hardware and software
software
hardware







## Slide 3: Outline
Von Neumann Machine Model
  Central Processing Unit (CPU)
  Memory
Instruction Set Architecture
  Taxonomy
  Operations and Data
  Instructions

## Slide 4: A Key Idea
Finite State Machines: function to be performed encoded in the state diagram
  Operation is “hardwired” into the circuits through the next state and output functions
Computer: function to be performed is encoded in a program that is stored in the computer’s memory
  Allows one to change the computer’s functionality without changing its hardware
  Both the program and data are stored in the same memory on the machine

## Slide 5: Von Neumann Machine Model: Main Elements
Access to “main memory” is slow, relative to CPU speeds (10x to 100x slower than access to memory within the CPU)
Virtually all computers first load data from main memory into the CPU, operate on the data (e.g., arithmetic) within the CPU, and then store the results back into main memory
  Has major impact in CPU and instruction set design
Central Processing Unit
(CPU)
Main
Memory
Data
local variables
global variables
dynamically allocated memory
function parameters, …
Program
Arithmetic, statements
If-then-else
Loops
Functions
I/O
Devices
Program and data stored in the same memory
Von Neumann Bottleneck
(aka “memory wall”)
Representation?
Notes: How the program is represented is greatly affected by the Von Neumann bottleneck

## Slide 6: Memory: Speed vs. Size
Tradeoff between memory speed (access time) and size; small memories are fast, large ones are slow
1 GHz clock: one clock cycle is 1x10-9 seconds or 1 nanosecond (ns)
Type of Memory | Typical Size | Typical Access Time
Single register | 32 to 64 bits | < 0.5 ns
Small register file | 32 x 32 bits | < 1.0 ns
Static RAM | 1 – 100 MBytes | ~1 ns – 50 ns
Dynamic RAM | 1 – 100 GBytes | ~50 ns – 150 ns
Disk / Flash Memory | 100 – 10,000 GBytes | ~1–10 ms (1M – 10M ns)
Analogy
(human terms)
~ second
~ minute
~ month
Here: only single registers and small register files are used within the CPU
  Access a single register or small register file in a single clock cycle
  Access to main memory requires many clock cycles

## Slide 7: Word and Word Length
Each computer is designed to operate on a unit of memory called a ”word”
  Typical word sizes today: 64 bits (we typically say the machine is a “64 bit architecture” to indicate the word size)
  Usually, ALU operates on ”word” sized data
  Memory addresses are typically one word
  Machine instructions are often one word
Computer can operate on other sizes of data, but more “effort” is required
  Data less than a word, e.g., byte, often involves extracting a byte from a word, and shifting to align data
  Data more than a word, e.g., long double, often involves processing one word at a time

## Slide 8: Mapping C to the Machine
C: Data Types
  int, short, long
  float, double
  char
  *int (pointers)
  arrays, struct
C: Program instructions
  Arithmetic, logic operations
  If-then-else, loops, function call/return
Machine Data Types
  Byte
  Word
  Half-word
  Double-word
  Floating point
  Address (word)
Machine Instructions
  Arithmetic, logic
  Branches, jumps, subroutine call/return
compiler
Central Processing Unit
(CPU)
Main
Memory
Data
local variables
global variables
dynamically allocated memory
function parameters, …
Program
Arithmetic, statements
If-then-else
Loops
Functions
I/O
Devices

## Slide 9: Machine Language
To a human the program looks like this (C code):
On unix systems, compile with –S flag
(% cc –S test.c) to see assembler
Main Memory
(e.g., 232 words)
…
11100101…
11100000…
00011100…
…
00000011…
…
machine instructions
data
To the hardware the program looks like this (machine code):
one word
Storage for variables
Assembler program: human readable version of machine code
Machine instruction
(assembler)
Machine instruction (typically 1 per word)
compiler
assembler
Data and instructions cannot be distinguished in memory (it’s all just 0s and 1s)!

## Slide 11: Instruction Set Architecture (Machine Language) Part 2: Instruction Set Architecture
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 12: Outline
Von Neumann Machine Model
  Central Processing Unit (CPU)
  Memory
Instruction Set Architecture
  Taxonomy
  Operations and Data
  Instructions

## Slide 13: Instruction Set Architecture
High level languages (HLL) such as C are too complicated for machines to execute directly
Machines can only execute a very simple set of instructions called the machine’s instruction set architecture (ISA)
  ISA defines all aspects of the CPU visible to the programmer/compiler
  Different CPUs have different ISAs (Intel x86, ARM, etc.)

## Slide 14: ISA Elements & the Program Counter
ISA defines key aspects (parameters) of the machine
  Number of bits in key data types (e.g., word)
  Number of bits in an address (determines maximum program size)
Defines machine instructions the CPU can execute
  Most machine instructions fit into a single word
CPU registers/memory visible to the programmer
  Program Counter (PC): address of the next instruction to be executed
CPU
Program Counter (PC)
Main Memory
…
program
code
word

## Slide 15: Machine Instructions
Each machine instruction contains
  An operation field (e.g., ADD)
  Zero or more operand(s) (address fields)
Major types of instruction set architectures
  Zero address (stack machine)
  One address (accumulator)
  Two address (register oriented)
  Three address (register oriented)
Register oriented architectures most common today
Machine instruction:
operation
operand(s)

## Slide 16: Zero Address: Stack Machine
CPU includes registers organized as a stack to hold operands, results
SP (stack pointer) register indicates top of stack
Not to be confused with the runtime stack used for functions (main memory)
Example: A = B + C
PUSH B // push M[B]
PUSH C // push M[C]
ADD // pop,pop,add,push
POP A // M[A]<-pop
Main Memory
…
A
B
C
CPU
Stack
SP
PC
Notation:
M[A]: data stored in memory location A

## Slide 17: One Address: Accumulator Machine
CPU includes one register called the accumulator (AC)
AC holds one operand and the result for arithmetic instructions
Example: A = B + C
LOAD B // AC<-M[B]
ADD C // AC<-AC+M[C]
STORE A // M[A]<-AC
Main Memory
…
A
B
C
CPU
Accumulator (AC)
PC

## Slide 18: Two/Three Address Architecture (Register Oriented)
CPU includes a small number of registers (e.g., R0 … R7)
Operands and result stored in registers
Example: A = B + C
LOAD R1,B // R1<-M[B]
LOAD R2,C // R2<-M[C]
ADD R3,R1,R2 // R3<-R1+R2
STORE R3,A // M[A]<-R3
CPU
General purpose registers
Main Memory
…
A
B
C
R0
R1
R2
R3
R4
R5
R6
R7
PC

## Slide 19: Other ISA Categorizations
“Complexity” of instruction set
  Reduced Instruction Set Computer (RISC)
    ARM
  Complex Instruction Set Computer (CISC)
    Intel x86
Memory Access (register-oriented architectures)
  Load/Store architecture: LOAD and STORE instructions are only ones that access data in memory; operands for other instructions are CPU registers
  Memory-to-memory architecture: many/most instructions can have operands and the result in memory
Instruction set design involves determining what computations occur most often in “typical” programs, and implementing them efficiently

## Slide 20: Instructions: Operations
A number of operations have similar counterparts as part of a programming language and as part of the machine instruction set. Can you name some of these? (See what you can come up with!)

## Slide 21: Instructions: Operations
Programming Language
Assignment
  temp = x;
Arithmetic
  result = x+y;
Conditionals
  if (a==b) {…}
  else {…}
Loops
  for(i=0;i<n;i++){…}
Function calls, return
  swap(int *a, int *b)
  return (…);
Machine Instruction Set
Data movement
  LDR R1,R2,offset
Arithmetic
  ADD R4,R5,R6
Conditionals
  Condition codes + branch
  BRz offset
Loops
  Implement w/ conditionals
Subroutine call, return
  JSR offset
  RET

## Slide 22: Accessing Data
Programming Language
Global variables
  int A;
Local variables and function parameters
  {int i; …}
Arrays
  double A[100];
Structures
  struct node {
  int data;
  struct node *next;
  };
Machine Instruction Set
One mechanism sufficient
(1) compute memory address (2) read/write memory
ex: addr=reg+offset
  offset field in instruction
Main Memory
…
…
CPU
reg
offset

## Slide 24: Instruction Set Architecture (Machine Language) Part 3: Instructions
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 25: Instructions
0 0 0 1
0 0 0
DR
S1
S2
Example encoding (16 bits)
0
15
An instruction is the most basic unit of computer processing and includes
The opcode: what the instruction does
The operands: what the instruction is done to
opcode
(0001 indicates ADD instruction)
unused
source register 1
destination
register
source register 2

## Slide 26: Instructions
Example:
Bits [15:12] specify opcode of 1: ADD
Bits [11:9] specify DR of 6: result will be stored in R6
Bits [8:6] specify SR1 of 2: operand 1 will be located in R2
Bits [2:0] specify SR2 of 6: operand 2 will be located in R6
0 0 0 1
0 0 0
DR
S1
S2
0
15
opcode
(0001 indicates ADD instruction)
unused
source register 1
destination
register
source register 2
0 0 0 1
0 0 0
1 1 0
0 1 0
1 1 0
0
15

## Slide 27: Instructions
For an instruction with this format:
What is the maximum number of different opcodes?
What is the maximum number of available registers for placing operands and results?
0 0 0 1
0 0 0
DR
S1
S2
0
15
opcode
(0001 indicates ADD instruction)
unused
source register 1
destination
register
source register 2

## Slide 28: Instructions
For an instruction with this format:
What is the maximum number of different opcodes? There are 4 bits for the opcode, so there can be at most 24=16 different opcodes.
What is the maximum number of available registers for placing operands and results? There are 3 bits for each register, so there can be at most 23=8 registers.
0 0 0 1
0 0 0
DR
S1
S2
0
15
opcode
(0001 indicates ADD instruction)
unused
source register 1
destination
register
source register 2

## Slide 29: Instruction cycle
Instructions proceed through a sequence of steps:
  FETCH: Memory’s address register loaded with contents of PC and PC is incremented, memory interrogated and instruction placed in memory data register, then loaded into instruction register
  DECODE: Instruction decoded to identify operation to perform and operands
  EVALUATE ADDRESS: Address of memory location that may be needed to perform the instruction is computed
  FETCH OPERANDS: Needed operands are obtained
  EXECUTE: Instruction is executed (e.g., addition)
  STORE RESULT: Result written to destination
Not all instructions use all steps, but all use steps 1-2

## Slide 30: Summary
Von Neumann architecture dominates, but suffers from von Neumann bottleneck
Program and data stored in memory, but must be brought into the CPU to be operated upon
  CPU registers reduce number of memory operations
Machine instruction set architecture defines what aspects of the hardware are visible to the programmer/compiler
More on instructions next week!