## Slide 1: Pipelining / Cache Intro Part 1: Pipelining Motivation
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 2: Outline: Pipelining
Motivation
Pipelining analogy and overview
Hazards

## Slide 3: Execution Time
A certain program on the LC-3 executes
1,000 ADD instructions
2,000 LDR instructions
500 BRz instructions (100 branch is taken (T), 400 not taken (NT))
Assume
  CPU has a 1 GHz clock
  Main Memory access requires 100 clock cycles
How long does it take to execute this program?

## Slide 4: LC-3 Control Unit (ADD, LDR, BRz Instructions)
MAR <- PC
PC <- PC+1
R=0
MDR<-M[MAR]
IR<-MDR
R=1
RD<-RS1+RS2
CC<-Sign
MAR<-RS1+IR[5:0]
R=0
MDR<-M[MAR]
RD <- MDR
CC<-Sign
R=1
IR[15:12]=ADD
IR[15:12]=LDR
PC<-PC+IR[8:0]
IR[15:12]=BRz
Z=1
Z=0
ADD:
1
1
1
1
100
104 clock cycles
LDR: 205 clock cycles
1
100
1
BRz (T): 105 clock cycles
1
1
BRz (NT): 104 clock cycles
Clock cycles?

## Slide 5: Total Execution Time
Instruction | Number | Clocks / Instruction | Clock Cycle Time | Total
ADD | 1000 | 104 | 1 ns | 104 µ sec
LDR | 2000 | 205 | 1 ns | 410 µ sec
BRz (taken) | 100 | 105 | 1 ns | 10.5 µ sec
BRz (not taken) | 400 | 104 | 1 ns | 41.6 µ sec
Total: 566.1 µ seconds

## Slide 6: Program Execution Time
Program execution time = N * CPI * cycle time
  N = total number of machine instructions executed
  CPI = clock cycles per instruction (average)
    Depends on frequency different instructions are executed
  Cycle time = 1 / clock rate
Previous example
  N = 3500
  CPI = 104*0.286 (ADD) + 205*0.571 (LDR) +
  105*0.0286 (BRz-T) + 104*0.114 (BRz-NT) = ~161.658
  Cycle time = 1 ns
  Same program execution time: 3500*161.658*1 ns ~= 566 µs
Memory access time dominates

## Slide 7: Improving Performance
Program execution time = N * CPI * cycle time
Can you think of some general strategies for improving performance (reducing program execution time)?

## Slide 8: Improving Performance
Program execution time = N * CPI * cycle time
Reduce N
  Improved instruction set design
  Compiler optimizations
Reduce CPI
  Redesign CPU (e.g., control unit state diagram)
  Instruction set design / compiler to change instruction mix (execute faster instructions more often)
  Pipeline
  Cache memory
Reduce cycle time (increase clock frequency)
  Faster circuits (Dennard scaling)

## Slide 10: Pipelining / Cache Intro Part 2: Pipelining Analogy
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 11: Outline: Pipelining
Motivation
Pipelining analogy and overview
Hazards

## Slide 12: CPU Pipeline
Here, five steps to process each instruction
Redesign data path and control unit so each step can be done in one clock cycle, rather than each instruction, assuming we do not need to wait for memory
Organize hardware into an assembly line to process instructions
Instruction Fetch
instructions
Read data
Write data
Memory
CPU
Decode
Fetch Operands
Execute
Store Result
PC
IR
Arithmetic
Circuits
Control Unit
Register File
Data Path

## Slide 13: Laundry Analogy
Consider laundry with four stages: washing, drying, folding, and stashing (putting away)
Each stage takes 30 minutes
Doing 4 sequential loads of laundry may look like this:
Task | 6pm | 6:30 | 7 | 7:30 | 8 | 8:30 | 9 | 9:30
A | Wash | Dry | Fold | Stash |  |  |  | 
B |  |  |  |  | Wash | Dry | Stash | Fold
 | 10pm | 10:30 | 11 | 11:30 | 12am | 12:30 | 1 | 1:30
C | Wash | Dry | Fold | Stash |  |  |  | 
D |  |  |  |  | Wash | Dry | Stash | Fold

## Slide 14: Pipelined Laundry
Laundry can be “pipelined”: break down the overall task of laundry into four smaller sub-components
With pipelined laundry, by when would the 4 loads of laundry be done?
Sequential laundry case:
Task | 6pm | 6:30 | 7 | 7:30 | 8 | 8:30 | 9 | 9:30
A | Wash | Dry | Fold | Stash |  |  |  | 
B |  |  |  |  | Wash | Dry | Stash | Fold
 | 10pm | 10:30 | 11 | 11:30 | 12am | 12:30 | 1 | 1:30
C | Wash | Dry | Fold | Stash |  |  |  | 
D |  |  |  |  | Wash | Dry | Stash | Fold

## Slide 15: Pipelined Laundry
With pipelined laundry, by when would the 4 loads of laundry be done?
By 9:30pm instead of 2am—a savings of 4.5 hours!
Task | 6pm | 6:30 | 7 | 7:30 | 8 | 8:30 | 9
A | Wash | Dry | Fold | Stash |  |  | 
B |  | Wash | Dry | Fold | Stash |  | 
C |  |  | Wash | Dry | Fold | Stash | 
D |  |  |  | Wash | Dry | Fold | Stash

## Slide 16: Instruction Processing Pipeline
What is the CPI?
If everything works properly, one instruction completes execution each clock cycle, yielding a CPI of 1.0
Instruction Fetch
Decode
Fetch Operands
Execute
Store Result
Hardware
fetch instr i
decode i
fetch op i
execute i
store i
clock cycle j
clock cycle j+1
clock cycle j+2
clock cycle j+3
clock cycle j+4
fetch i+1
decode i+1
fetch op i+1
execute i+1
fetch i+2
decode i+2
fetch op i+2
fetch i+3
decode i+3
fetch i+4
Pipelining is a form of instruction-level parallelism (ILP): done by compiler and hardware, not programmer

## Slide 17: Speedup from Pipelining
What are some factors that affect the speedup achieved by pipelining?
  Time to “fill” and “drain” the pipeline when starting and stopping
  Number of stages
  Limited by the slowest pipeline stage
  Unbalanced lengths of pipe stages can reduce speedup
  Dependences—might have to stall (e.g., wait for result from earlier stage)

## Slide 19: Pipelining / Cache Intro Part 3: Pipeline Hazards
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 20: Outline: Pipelining
Motivation
Pipelining analogy and overview
Hazards

## Slide 21: Types of Pipeline Hazards
Pipelining has the potential to get us into trouble:
  Structural hazards attempt to use the same resource in two different ways at the same time
  Control hazards attempt to make a decision (e.g., branch) before a condition is evaluated
  Data hazards attempt to use an item (e.g., a result needed to execute an instruction) before it is ready

## Slide 22: Laundry Hazards
Below are some potential hazards that could be encountered during pipelined laundry. What type of hazard is each?
  A combined washer/dryer device replaces the separate washer and dryer
  A dirty item is being washed and before proceeding it is necessary to know if it came out clean
  The person doing the folding is busy doing the stashing
  One sock of a pair is in the dryer and one is in the washer

## Slide 23: Laundry Hazards
Below are some potential hazards that could be encountered during pipelined laundry. What type of hazard is each?
  A combined washer/dryer device replaces the separate washer and dryer -> Structural hazard
  A dirty item is being washed and before proceeding it is necessary to know if it came out clean -> Control hazard
  The person doing the folding is busy doing the stashing -> Structural hazard
  One sock of a pair is in the dryer and one is in the washer -> Data hazard (cannot fold and put away until both are together)

## Slide 24: Issue: Structural Hazard
Structural hazard: two different stages may need to access the same hardware resource at the same time
Instruction Fetch
Decode
Fetch Operands
Execute
Store Result
fetch instr i
decode i
fetch op i
execute i
store i
clock cycle j
clock cycle j+1
clock cycle j+2
clock cycle j+3
clock cycle j+4
fetch i+1
decode i+1
fetch op i+1
execute i+1
fetch i+2
decode i+2
fetch op i+2
fetch i+3
decode i+3
fetch i+4
LDR instruction reads memory
instruction fetch reads memory
Solutions
One stage waits (stall pipeline – insert no-op instruction at fetch stage; aka insert a “bubble”)
Replicate resource (separate instruction & data caches)
LDR instruction
R<-M[BR+off]

## Slide 25: Data & Instruction Cache
Complication: Programs may overwrite instruction!
What if the instruction resides in both caches?
Data write must invalidate the instruction if it resides in the instruction cache
Instruction Fetch
CPU
Decode
Fetch Operands
Execute
Store Result
PC
IR
Arithmetic
Circuits
Control Unit
Register File
Data Path
Main
Memory
(MM)
Instruction Cache
Data Cache

## Slide 26: Issues: Branch Instructions (Control Hazard)
Branch Prediction
CPU “guesses” outcome of the branch (taken/not taken)
Abort instruction execution(s) if guess is wrong
Instruction Fetch
Decode
Fetch Operands
Execute
Store Result
Hardware
fetch instr i
decode i
fetch op i
execute i
store i
clock cycle j
clock cycle j+1
clock cycle j+2
clock cycle j+3
clock cycle j+4
fetch i+1
decode i+1
fetch op i+1
execute i+1
fetch i+2
decode i+2
fetch op i+2
fetch i+3
decode i+3
fetch i+4
fetch branch instr. (e.g., BRz)
result of branch (taken or not taken) known here
if branch is taken, we fetched the wrong instruction!

## Slide 27: Issue: Data Hazard
Data hazard: the result of one instruction is stored in a register and is needed by a later instruction (e.g., next one) but the needed value is not stored into the register in time.
Instruction Fetch
Decode
Fetch Operands
Execute
Store Result
Hardware
fetch instr i
decode i
fetch op i
execute i
store i
clock cycle j
clock cycle j+1
clock cycle j+2
clock cycle j+3
clock cycle j+4
fetch i+1
decode i+1
fetch op i+1
execute i+1
fetch i+2
decode i+2
fetch op i+2
fetch i+3
decode i+3
fetch i+4
Compute memory address
LDR R1, … (R1 <- M[…])
ADD … R1 …. (uses data in R1)
Read memory
Store data into R1
Decode LDR instruction
Read R1: reads the old value of R1!

## Slide 28: Data Forwarding
PC
IR
Register
File
MDR
MAR
RAM
1
1
2
fetch op i
execute i
store i
clock cycle j+2
clock cycle j+3
clock cycle j+4
decode i+1
fetch op i+1
execute i+1
fetch i+2
decode i+2
fetch op i+2
fetch i+3
decode i+3
fetch i+4
Read memory
Modify datapath: also immediately forward data to where it’s needed (here, ALU for ADD instr.)
Caveat: Pipelines add complications to the design; in some cases it may be necessary to delay processing of some instructions

## Slide 29: Pipelining Summary
Execution time = N * CPI * cycle time
Pipelines a general approach using concurrent processing (assembly line)
  CPU: instruction processing to reduce CPI
  Can be used in software also (a form of parallel processing)
CPU implementation requires consideration of hazards
  Structural hazards (resource conflicts)
  Control hazards (branches)
  Data hazards (data dependencies)

## Slide 31: Pipelining / Caches Part 4: Basic Concepts of Caches
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 32: Recall LC-3 Control Unit
MAR <- PC
PC <- PC+1
R=0
MDR<-M[MAR]
IR<-MDR
R=1
RD<-RS1+RS2
CC<-Sign
MAR<-RS1+IR[5:0]
R=0
MDR<-M[MAR]
RD <- MDR
CC<-Sign
R=1
IR[15:12]=ADD
IR[15:12]=LDR
PC<-PC+IR[8:0]
IR[15:12]=BRz
Z=1
Z=0
ADD:
1
1
1
1
100
104 clock cycles
LDR: 205 clock cycles
1
100
1
BRz (T): 105 clock cycles
1
1
BRz (NT): 104 clock cycles
Clock cycles?
Memory access time dominates!

## Slide 33: Cache Memory
Fundamental principle
  Access to large memories takes a long time
  Access to small memories is much faster
Caching is a technique to try to get the best of both worlds: fast access AND large memory
  Keep frequently used items in small, high-speed memory called a cache
  Only access slower memory when the required instructions or data do not reside in the cache

## Slide 34: Cache Memory
Small, high-speed memory
  Access time usually less than one clock cycle
  Cache holds fixed sized blocks (e.g., 64 bytes)
Interface to cache same as main memory (CPU issues read/write operations)
Memory read operation (address A)
  If contents of memory address A (M[A]) is in cache (hit) read M[A] from cache
  If M[A] not in cache (miss), load data from MM into cache, and return data to CPU (usually need to delete other data from cache to make room)
PC
IR
Control
Unit
Register
File
Main
Memory
(MM)
Cache
Memory

## Slide 35: Performance
Suppose:
  Cache access time (hit) = 1 ns
  MM access time (miss; includes time to access cache) = 100 ns
  90% cache hit rate (or 10% miss rate)
Access time
  What is the average access time?
  How much faster is the average access time with this cache than having to access main memory? (0% cache hit rate)
  How much slower is the average access time with this cache than if all items were in the cache (0% miss rate)

## Slide 36: Performance
Suppose:
  Cache access time (hit) = 1 ns
  MM access time (miss) = 100 ns
  90% cache hit rate (or 10% miss rate)
Access time
  Average access time = 0.9*1 + 0.1*100 ns = 10.9 ns
  100ns/10.9ns ~= 9x faster than MM (w/o cache)
  But, 10.9ns/1ns ~= 11x slowdown compared to cache hit
Misses are very costly, even if not very frequent
Cache performance has a large impact on program execution time

## Slide 37: Why Do Caches Work?
Cache size << MM size
  Example: MM: 8 Gbytes; Cache: 256 KBytes
  Cache tiny compared to main memory (<< 1%)
  If memory accesses randomly distributed, chances of cache hit are very small!
Works well in reality because of locality of reference
  Spatial locality: If a memory address is referenced, chances are good a location near that one will be referenced soon
    Sequential machine instructions
    Variables and parameters on runtime stack
  Temporal locality: If a memory location is referenced now, chances are good it will be referenced again soon in the near future
    Instructions within a loop
    Local variables and other data structures
But cache misses are still very expensive!

## Slide 38: Program Locality
Things that tend to yield good locality
  Loops, especially small ones
  Stack frame data (locals, parameters, return value)
  Structures, especially small ones that are accessed often
Things that tend to yield poor locality
  Large arrays where elements accessed “randomly”
  Large dynamically allocated data structures (malloc)
  Excessive use of function calls (e.g., system calls)

## Slide 39: Cache vs. Register File
Register File
Small, fast memory physically near CPU
Only holds data (not instructions)
Small size (e.g., 32 or 64 memory words)
Very fast access
Visible to instruction set
Cache Memory
Small, fast memory physically near CPU
Holds instructions and data
Moderate size: Kbytes to Mbytes
Somewhat slower access, but still 1 clock cycle for smaller caches
Not visible to instruction set (interface to CPU same as main memory)

## Slide 40: Cache Summary and Next Time
Caches improve memory access speed
Reliant on temporal and spatial locality of reference
Many issues still to discuss:
  Cache placement, replacement, write policy
  Multiple caches
  Cache-like options for disk access
  Caching issues for multiprocessors