## Slide 1: Machine Organization: Implementation of the ISA Part 1: CPU Organization and LC-3
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 2: Levels of Abstraction in Computers
Defines interface between hardware and software
Implementation of the instruction set architecture
Application
(word processor, simulator, web browser, …)
Algorithms
(sorting, optimization, equation solver, …)
Programming Language
(C, FORTRAN, Matlab, Java, …)
Machine Instruction Set Architecture
(Intel i86, ARM, …)
Machine Organization
(Main memory, registers, adders, …)
Logic Gates
(NAND, NOR, inverter, …)
Transistors
(CMOS, NMOS, …)
Physics (Semiconductors)
(electrons, holes, …)
Operating System
(UNIX, Windows, iOS, …)








## Slide 3: Road Map
Central processing unit (CPU)
(microprocessors)
Memory
Sequential circuits
electricity
combinational logic
logic gates
circuits
transistors
materials

## Slide 4: Outline
Overall Organization of CPU
  Data Path
  Control Unit
Overview of LC-3 Data Path Design
LC-3 Instruction Set: Data Path Examples
  Arithmetic/logical
  Memory
  Control
Control Unit Design
  Finite state machine

## Slide 5: Interpreters
An interpreter is need to perform (execute) the instructions specified by the program
Machine language is interpreted by CPU hardware
  Fast, efficient execution
  Must use a compiler to translate high level language code to machine language code
  Examples: C, C++, FORTRAN, Java, …
A program (software interpreter) could also be used to interpret (execute) the program
  Slower, less efficient execution
  Easier (faster) to program (no compilation needed)
  Examples: Matlab, Python, Java, …

## Slide 6: A View of Systems
Action
Control
control
signals
status
signals
Data
Path
Control Unit
(Finite State Machine)
control
signals
status
signals
Computer System (CPU)
gas pedal, brake,
steering wheel
speedometer
fuel gauge
Automobile
The data path includes functional units that process data (e.g., ALUs) together with registers and buses.
The control unit directs the memory, ALU, and I/O responses to instructions.

## Slide 7: Von Neumann Machine Model
Central Processing Unit (CPU)
Main
Memory
I/O
Devices
(keyboard, display, disk)
Data Path
Control Unit
The CPU basically only does one thing: move bits from one place (register or memory) to another
Sometimes the bits are moved through a circuit that can perform arithmetic
  Arithmetic/Logic Unit (ALU)
  Here, ALU is purely combinational logic (no memory)

## Slide 8: Outline
Overall Organization of CPU
  Data Path
  Control Unit
Overview of LC-3 Data Path Design
LC-3 Instruction Set: Data Path Examples
  Arithmetic/logical
  Memory
  Control
Control Unit Design
  Finite state machine

## Slide 9: Instruction Set Architecture
The ISA specifies all information about the computer that the software needs to be aware of
  Memory organization
  Register set
  Instruction set
    Opcodes
    Data types
    Addressing modes
This information is available to a programmer when writing in the computer’s own machine language
We will focus on the fictional LC-3 computer
Last class we had a quick look; today we’ll take a deeper dive

## Slide 10: LC-3 Memory and Registers
Address space: 216 locations (16-bit addresses)
Addressability: 16 bits (what each memory location stores)
Normal unit of data processed in the LC-3 is 16 bits = one word, so LC-3 is word-addressable
Accessing items from memory is typically slow, leading to the need for fast temporary storage locations that can be accessed in one clock cycle
LC-3 has 8 general-purpose registers, each of which can store one word
GP registers are uniquely identifiable as R0-R7

## Slide 11: Data Path: Memory Elements
Program Counter (PC)
General purpose registers
Condition code register
Registers are also needed to hold
  Address used for memory reads/writes (MAR)
  Data read to/written from main memory (MDR)
  Instruction now being processed (IR)
16 bits
…
M[addr]: Main Memory
0000
0001
0002
FFFF
216 = 65,536
CPU
Registers
0
1
2
3
4
5
6
7
16 bits
PC
N
Z
P
Condition
Code (CC) register
The data path consists of all the logic structures that combine to process information in the core of the computer.

## Slide 12: Memory Interface
MAR: Memory Address Register (16 bits) read from/write to this address
  Control signal LMAR: assert to load MAR register
MDR: Memory Data Register (16 bits) information stored in that location
  Control signal LMDR: assert to load MDR register
Main Memory
  Control signal MRd – assert to read memory: MDR<-M[MAR]
  Control signal MWr – assert to write memory: M[MAR]<-MDR
  Status signal R: Ready – asserted when memory operation completed
MAR
MDR
Main Memory
Random Access Memory
(65,536 x 16)
MRd
MWr
R
address
data
CPU
(data path)
Memory
System
LMAR
LMDR
Set up for read/ write ops

## Slide 13: Multiport Register File
Used to implement 8 CPU registers in LC-3
Can simultaneously perform multiple memory operations in a single clock cycle (e.g., ADD)
  Two read operations
  One write operation
  Can read/write the same register in a single instruction
Register
File
RRd1
RRd2
RWr
1
2
A1
A2
AWr
Address
(how many bits?)
Control signals
data (read)
data (read)
data (write)
Notes: Implementation: straightforward extension of RAM discussed earlier; just need 3 decoders

## Slide 14: Multiplexer Circuit
Combinational logic (no storage inside multiplexer)
Above is a 4:1 one-bit multiplexer (mux)
The circuit can be replicated for inputs with more bits
logical
view
decoder
select
implementation
in0
in1
in2
in3
00
01
10
11
out
circuit
component
select
in0
in1
in2
in3
out
select
in0
in1
in2
in3
out
out=in[select]

## Slide 15: Multiport Register File Implementation
Write
D
WE
Q
DWi
…
…
Write decoder
AWr
RRd1
DR1i
…
…
DR2i
Read 1 decoder
A1
Read 2 decoder
A2
Switch
C = 0 open
C = 1 closed
C
RRd2
write
read register port 1
read register port 2

## Slide 17: Machine Organization: Implementation of the ISA Part 2: More on LC-3 Instruction Set
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 18: Outline
Overall Organization of CPU
  Data Path
  Control Unit
Overview of LC-3 Data Path Design
LC-3 Instruction Set: Data Path Examples
  Arithmetic/logical
  Memory
  Control
Control Unit Design
  Finite state machine

## Slide 19: LC-3 Instruction Set
Instruction set is defined by its set of opcodes, data types, and addressing modes (determine whether the operands are located)
The choice of which instructions to include or leave out of a new ISA depends on many factors
Opcodes specify the types of operation, operands specify on what data the operation is performed
LC-3 ISA has 15 instructions, each with a unique opcode specified with the first 4 bits of an instruction
LC-3 only supports integers (no other data type)

## Slide 20: Three Types of Instructions
Three types of instructions: operate (arithmetic/ logical), data movement, and control
Categorize the following LC-3 operations as best you can:
ADD
AND
BR (branch)
JMP (jump)
JSR (jump to subroutine)
LD (load)
NOT
RET (return from subroutine)
ST (store)
TRAP (system call)

## Slide 21: Three Types of Instructions
Three types of instructions: operate (arithmetic/ logical), data movement, and control
Categorize the following LC-3 operations as best you can:
But wait! You may be thinking—there are not 15 of these!
There are variations for addressing modes… next topic
Control
BR (branch)
JMP (jump)
JSR (jump to subroutine)
RET (return from subroutine)
TRAP (system call)
Data Movement
LD (load)
ST (store)
Operate
ADD
AND
NOT

## Slide 22: LC-3 Instructions
Store “flavors”
Load “flavors”
Load “flavors”

## Slide 23: Addressing Modes
Mechanism for specifying where the operand is located, generally one of the following:
  In memory
  In a register
  Within the instruction (literal or immediate operand)
LC-3 supports 5 addressing modes:
  Immediate: operand is in the instruction
  Register: operand is in a register
  PC-relative: operand is located an offset from the PC
  Indirect: PC-relative address is a pointer to the operand
  Base + offset: operand is located an offset from address in register
Operate instructions use only immediate and register modes

## Slide 24: Condition Codes
Sequence of instructions may change depending on previously generated result
LC-3 sets or clears 3 single-bit registers each time one of the GP registers is written (arithmetic/logical and load instructions): N, Z, P
The condition of that bit can be used by control instructions to change the sequence of instructions

## Slide 26: Machine Organization: Implementation of the ISA Part 3: LC-3 Data Path Examples
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 27: Instructions to Be Implemented
Instruction Processing
Fetch instruction to be executed: M[PC] and increment the PC
Decode instruction (check opcode)
Execute instruction
  Evaluate address
  Fetch operands
  Perform operation (e.g., add)
  Store result
Go back to step 1
ADD DR, S1, S2 // DR <- S1 + S2
LDR DR, BR, offset // DR <- M [BR + offset]
BRz offset // if (Z bit set)
// PC <- PC+1+offset
We will look at these in detail and look at a few others briefly

## Slide 28: LC-3 ADD Instruction
0 0 0 1
0 0 0
DR
S1
S2
Encoding (16 bits)
0
15
12
11
9
8
6
2
Notation: IR[x:y] means bits x, x-1, … y or IR register
IR[15:12] is the opcode; IR[8:6] indicates register S1
Arithmetic
ADD DR, S1, S2 // DR, S1, S2 are registers
// DR <- S1 + S2
// set N, Z, P if result negative, zero, or positive, respectively
opcode
(0001 indicates ADD instruction)
unused
source register 1
destination
register
source register 2

## Slide 29: LC-3 ADD Instruction
0 0 0 1
0 0 0
0 0 1
1 0 0
1 0 1
Encoding (16 bits)
0
15
12
11
9
8
6
2
ADD R1, R4, R5
// R1 <- R4 + R5
// set N, Z, P if result negative, zero, or positive, respectively
ADD performs 2s complement addition
ADD can also specify an immediate operand instead of a second register: 0001 001 100 1 11110 will store in R1 the sum of R4 and -2

## Slide 30: LC-3 Logical Instructions
See if you can determine the effects of the following LC-3 instructions.
1 0 0 1
1 1 1
DR
S1
1 1 1
0
15
12
11
9
8
6
2
Must contain all 1’s
0 1 1
1 0 1
NOT
0 1 0 1
0 0 0
DR
S1
0 1 0
0
15
12
11
9
8
6
2
Must be 0’s
1 1 0
0 1 1
AND
S2
7 | 721C
6 | 382A
5 | 0001
4 | 0004
3 | F0F0
2 | E1E1
1 | 02A3
0 | B782
Registers

## Slide 31: LC-3 Logical Instructions
See if you can determine the effects of the following LC-3 instructions.
1 0 0 1
1 1 1
DR
S1
1 1 1
0
15
12
11
9
8
6
2
Must contain all 1’s
0 1 1
1 0 1
NOT
0 1 0 1
0 0 0
DR
S1
0 1 0
0
15
12
11
9
8
6
2
Must be 0’s
1 1 0
1 0 0
AND
S2
7 | 721C
6 | 382A
5 | 0001
4 | F0F0
3 | 0004
2 | E1E1
1 | 02A3
0 | B782
Registers
Store the complement of R5 in R3: FFFE
Store the bitwise AND of R4 and R2 in R6: E0E0

## Slide 32: LC-3 NOT Instruction
1 0 0 1
1 1 1
DR
S1
1 1 1
0
15
12
11
9
8
6
2
Must contain all 1’s
0 1 1
1 0 1
NOT
Store the complement of R5 in R3: FFFE
Note that only one input of the two available to the ALU is used.

## Slide 33: LC-3 LDR Instruction
Memory
LDR RD, RS1, offset // RD <- M [RS1 + offset]
// sign extend offset
0 1 1 0
RD
RS1
offset
Encoding (16 bits)
opcode
dest. reg.
base reg.
6 bit offset
16 bits
…
Main Memory
0000
0A10
0A11
FFFF
0A12
Registers
0A10
0
1
2
3
4
5
6
7
16 bits
0
0
1
Condition
Code (CC) bits
N
Z
P
LDR R1, R5, 2 // R1 <- M[R5 + 2]
…
0023
0023
0
15
12
11
9
8
6
5
0 1 1 0
0 0 0
0 1 0
0 0 1
1 0 1

## Slide 34: LC-3 LDR Instruction
0023
LDR
Load into R1 the contents of the memory location specified by the sum of R2 and 29: M[R2+29]
Here R2 contains x2345. Adding sign-extended 29 (x001D) gives x2362; this is loaded into the MAR.
M[2362] is loaded into the MDR and then into R1.
0110
001
010
0 1 1 0
DR
S1
1 0 1
0 1 1
0
15
12
11
9
8
6
2
0 0 1
0 1 0

## Slide 35: Other LC-3 Load Instructions
There are a total of four load instructions in the LC-3 instruction set.
LDR (0110):
  Base + offset: memory address is a 6-bit offset from an address in register
LD (0010):
  PC-relative: memory address is located a 9-bit offset from the incremented PC
LDI (1010):
  Indirect: PC-relative (9-bit offset) address is a pointer to the memory address
LEA (load effective address) (1110):
  Immediate: does not access memory; loads into the specified register the address formed from the incremented PC and the 9-bit value in the instruction

## Slide 36: LC-3 BRz Instruction
Control
BRz offset // if (Z bit set) PC <- PC+1+offset
// sign extend offset
// previous instruction sets Z
0 0 0 0
0 1 0
offset
Encoding (16 bits)
opcode
Test Z bit
9-bit offset
16 bits
BRz -3
// if Z bit is set, PC <- PC-2
…
Main Memory
FFFF
F112
F111
0000
F110
…
BRz -3
0
15
12
11
9
8
0 0 0 0
1 1 1
1 0 1
0 1 0
1 1 1

## Slide 37: LC-3 BRz Instruction
0 0 0 0
0 1 0
0 1 1 0 1 1 0 0 1
opcode
Test Z bit
9-bit offset
0
15
12
11
9
8
BRz instruction: if Z bit is set, then load the PC with the new address.
The new address is the incremented PC + the sign-extended 9-bit offset.
Here the incremented PC is x4028.
The new address (used only if Z bit is set) is x4028 + x00D9 = x4101.

## Slide 38: More on LC-3 BR
What if the test bits in the instruction were set as follows?
What if the test bits in the instruction were set as follows?
0 0 0 0
1 1 1
0 1 1 0 1 1 0 0 1
opcode
Test bits
9-bit offset
0
15
12
11
9
8
0 0 0 0
0 0 0
0 1 1 0 1 1 0 0 1
opcode
Test bits
9-bit offset
0
15
12
11
9
8

## Slide 39: More on LC-3 BR
With all three bits set, the branch would be taken every time, so the instruction becomes an unconditional branch.
With none of the bits set, the branch would never be taken, so the instruction becomes a no-op.
0 0 0 0
1 1 1
0 1 1 0 1 1 0 0 1
opcode
Test bits
9-bit offset
0
15
12
11
9
8
0 0 0 0
0 0 0
0 1 1 0 1 1 0 0 1
opcode
Test bits
9-bit offset
0
15
12
11
9
8

## Slide 41: Machine Organization: Implementation of the ISA Part 4: Control Unit Design
For use in Fall 2020 CSE6010/CX4010 only
Not for distribution

## Slide 42: Outline
Overall Organization of CPU
  Data Path
  Control Unit
Overview of LC-3 Data Path Design
LC-3 Instruction Set: Data Path Examples
  Arithmetic/logical
  Memory
  Control
Control Unit Design
  Finite state machine

## Slide 43: Partial LC-3 Data Path (ADD, LDR, BRz instructions)
PC
IR
Register
File
MDR
MAR
Main Memory (RAM)
MRd
MWr
R
1
N
Z
P
IR[8:0]
(sign ext.)
IR[5:0]
(sign ext.)
Multiplexer
16 bits
1 bit
KEY
LMDR
LMAR
LPC
LIR
MMAR
MPC
MALU
MRF
“add”
ALUop
LCC
RRd1
RRd2
RWr
1
2
IR[2:0]
IR[8:6]
IR[11:9]

## Slide 44: LC-3 Control Unit (ADD, LDR, BRz Instructions)
MAR <- PC
PC <- PC+1
R=0
MDR<-M[MAR]
IR<-MDR
R=1
RD<-RS1+RS2
CC<-Sign
MAR<-RS1+IR[5:0]
R=0
MDR<-M[MAR]
RD <- MDR
CC<-Sign
R=1
IR[15:12]=ADD
IR[15:12]=LDR
PC<-PC+IR[8:0]
IR[15:12]=BRz
Z=1
Z=0

## Slide 45: Control and Status Signals
Control Signals
(FSM outputs)
MRd: read memory
MWr: write memory
LPC: load PC
LIR: load IR
LMAR: load MAR
LMDR: load MDR
MPC: PM mux
MMAR: MAR mux
MRF: register file mux
MALU: ALU mux
ALUop: ALU operation
LCC: load condition codes
Status Signals (FSM inputs)
R: Memory operation completed
IR[15:12]: opcode
N: N bit of condition code
Z: Z bit of condition code
P: P bit of condition code
Control Signals (cont.)
RRd1: read RF port 1
RRd2: read RF port 2
RWr: write RF
main
memory
load
register
mux
control
register
file
misc.

## Slide 46: LC-3 Control Unit (ADD, LDR, BRz Instructions)
RRd1; RRd2; MALU=RF; ALUOp=add; LCC; MRF=ALU; RWr;
RRd1; MALU=IR ALUOp=add; MMAR=ALU; LMAR
R=0
MRd; LMDR
MRF=MDR; RWr; LCC
R=1
IR[15:12]=ADD
IR[15:12]=LDR
MPC=IR; LPC
IR[15:12]=BRz
Z=1
Z=0
MMAR=PC; LMAR; MPC=1; LPC
R=0
MRd; LMDR
LIR
R=1

## Slide 47: Notes
The data path and control unit shown so far only represent the realization of three machine instructions; one must continue design process for the full instruction set
It is convenient to define a “bus” in the data path to carry signals among multiple sources and destinations of data
  Only one source device can put data on bus at one time!
…
…
bus
source
devices
destination
devices

## Slide 48: LC-3 Data Path

## Slide 49: Summary: CPU Design Process
CPU = Data Path + Control Unit
Data path design: determine what components you need
  Memory visible to machine code programmer/compiler (PC, registers, condition codes)
  Memory and memory interface (MAR, MDR)
  Instruction Register (IR)
  ALU(s)
Control Unit: design finite state machine
  Implement instruction processing cycle: Instruction Fetch, decode, operand fetch, execute, store result
  Determines interconnection among the components in the data path design